## Slide 1
DAQ Projects
Spring 2022

## Slide 2: Spring 2022 Plans
Plan to meet in person at the SCC
  Probably will meet in one of the classrooms
  For those that do not have SCC access, I will give instructions on how to get there and can let people into the building
Tuesday, Thursday – 8-11
Sunday 4-7

## Slide 3: Goals over break
Design Review of Aux Daq V2
Determine issue with Shock Dyno, make V2?
Continue work on embedded software for dashboard
Software for temp sensor

## Slide 4: Spring testing
Now we are beginning the phase where we are starting to actually begin to do testing
The rest of the slides are the outline for what tests we plan on running in the spring

## Slide 5: Chassis team
Chassis Stiffness Test
  Need a load cell
Vibration Test
  High sampling rate on IMU (~150-200 Hz)
Strain Gauge on Chassis Members
  Need to run strain gauge tests
  Measure voltage with aux daq

## Slide 6: Suspension team
LDS Sensors on shocks
IMU on car
Shock Dyno
Measure steering wheel position
Strain gauges on uprights
Strain gauge on steering wheel
ARB Torsional Stiffness Test
  Need load cell to measure force/torque
  Need a way to measure angular deflection

## Slide 7: Driver controls team
Brake Line Pressure Measurement
Throttle/Brake Pedal Position
Braking Force Transfer
  Need 2 load cells to measure torque
Driveshaft slip test
  Need load cell to measure torque and brake pressure sensors

## Slide 8: Drivetrain team
Engine RPM Measurement
  Need optical encoder on case and magnetically coupled encoder
Transfer Case RPM Measurement
Car Timing Measurement (Light Gates)
Engine Dyno Tests
Driveshaft Torsional Deflection
  Need two inline quadrature encoders
Driveshaft Torsional Stiffness Test

## Slide 9: DriveTrain Team (cont.)
CVT Spring Rate Test
  Need a load cell
Car Acceleration Curve Measurement
  IMU to measure acceleration and speed sensor to measure speed
CVT Belt Temperature Measurement
  IR sensor to measure belt directly
Transfer Case Temperature Measurement
  Temperature sensor for oil temp
Driveshaft Strain Measurement
  Use strain gauge on driveshaft